 AD57xx Library overview

# Overview AD57 library calls.

## void debug(bool act)
enable / disable debug information and display library version.
## void reset()
Normally after applying power the DAC will perform a power-up reset setting all values to zero. Reset will perform a soft reset by setting all to zero as well.
## bool begin(uint8_t dac, uint8_t range, bool comp2 = BINARY)
MUST BE CALLED at begining. To initialize the SPI interface.
For simplicity it sets range for the first DAC, which can be added / changed with setRange()

The optional comp2 allows to 2scomp setting when using bipolar output mode (see remark 1 in the appendix B and sketch.)

Will return true if all was set OK, else false.
## uint8_t getControl()
read control register value for instructions
## uint16_t getDac(uint8_t dac)
Reads dac channel register value. If dac is DAC_AB, we can not obtain both DAC-A and DAC-B at the same time. It will obtain DAC_A only in that case.
## uint8_t getPower()
get channel power status, return
0 = DAC channel A and channel B are powered down
1 = DAC channel A powered-up
2 = DAC channel B powered-up
3 = DAC channel A and B are both powered-up */
## uint8_t getRange(uint8_t dac)
read output range value for dac channel.

Will return p5V, p10V, P108V, pn5V, pn10V or pn108v (see appendix A.)

If dac is DAC_AB, we can not obtain both DAC-A and DAC-B at the same time. It will obtain DAC_A only in that case.

## uint16_t getStatus()
get status information
Return :
0	// no error / nothing set
stat_err_TO	// ERROR Therminal overheat shutdown
stat_err_CA	// ERROR Overcurrent DAC-A
stat_err_CB	// ERROR Overcurrent DAC-B
stat_TS	// Therminal shutdown is enabled in control
stat_CLR	// Clr is set in control register in control
stat_CLAMP	// clamp / Overcurrent protection is enabled in control
stat_SDO	// Serial data out is disabled (how did you get the output ??)
## uint16_t getError()
get error information only
Return :
0	// no error / nothing set
stat_err_TO	// ERROR Therminal overheat shutdown
stat_err_CA	// ERROR Overcurrent DAC-A
stat_err_CB	// ERROR Overcurrent DAC-B
## void setControl(char opcode, uint16_t instruct = 0x0)
setsControl register
Opcode : OP_NOP, OP_INSTR, OP_CLR, OP_LOAD
only when the opcode is OP_INSTR, an instruct-value is needed, see Appendix A
## void setDac(uint8_t dac, uint16_t value, bool load = 1)
set DAC channel value. Dac is either DAC_A, DAC_B or DAC_AB
The optional load argument ‘load’, if set to 0 will NOT load the value to the register, but the use must call loadDac(). This enables to set DAC_A and DAC_B first with seperate values and then enable both at the same time (if needed). See example sketch.
## void loadDac()
Will load the updated value to the DAC register in case optional argument ‘load’ was used in SetDac or with the LDAC pin held HIGH.
## void setPower(uint8_t setting)
Power-up or power-down a DAC channel. See Appendix A for options.
## void setRange(uint8_t dac, uint8_t value)
set output range value for dac channel.
Values can be p5V, p10V, P108V, pn5V, pn10V or pn108v (see appendix A.)
## void setOutput(uint8_t act)
Hardware load control. Is optional and only available if a pin has been set. For ‘act’ see appendix A. For more info see remark 2 in the appendix B and example sketch.
# Appendix A. Constants to use
/* define the type of AD57xx is connected in the sketch: DacType = */
#define AD5722	1 // 12 bit
#define AD5732	2 // 14 bit
#define AD5752	3 // 16 bit

/* output range selections : use with setRange() */
#define p5V	0 // +5V
#define p10V	1 // +10V
#define p108V	2 // +10.8V
#define pn5V	3 // +/-5V
#define pn10V	4 // +/-10V
#define pn108V	5 // +/-10.8V

/* channels use where 'dac' is requested */
#define DAC_A	0
#define DAC_B	2
#define DAC_AB	4

/* control register opcode : use with setControl() */
#define OP_NOP	0 // do nothing (needed for reading)
#define OP_INSTR	1 // combine with instruction(s) (see below)
#define OP_CLEAR	4 // clear DAC values (as defined by CLR instruction)
#define OP_LOAD	5 // load new DAC values

/* control register instruction : !! Opcode MUST be set OP_INSTR !!!! */
#define SET_TSD_ENABLE	0x8 // enable terminal shutdown command
#define SET_CLAMP_ENABLE	0x4 // enable the current-limit clamp.
#define SET_CLR_SET	0x2 // define the DAC values after OP_CLEAR
#define SET_SDO_DISABLE	0x1 // disable the SDO output

#define STOP_TSD_ENABLE	0x80 // disable terminal shutdown command
#define STOP_CLAMP_ENABLE	0x40 // disable the current-limit clamp.
#define STOP_CLR_SET	0x20 // define the DAC values after OP_CLEAR
#define STOP_SDO_DISABLE	0x10 // enable the SDO output

/* power register settings : use with setPower()*/
#define SET_PUA	0x1 // power-up DAC-A.
#define SET_PUB	0x2 // power-up DAC-B
#define STOP_PUA	0x4 // power-down DAC-A.
#define STOP_PUB	0x8 // power-down DAC-B.

/* define status feedback getStatus() */
#define stat_err_TO	0x1 // ERROR Therminal overheat shutdown
#define stat_err_CA	0x2 // ERROR Overcurrent DAC-A
#define stat_err_CB	0x4 // ERROR Overcurrent DAC-B
#define stat_TS	0x8 // Therminal shutdown is enabled in control
#define stat_CLR	0x10 // Clr is set in control register in control
#define stat_CLAMP 0x20 // clamp / Overcurrent protection is enabled in control
#define stat_SDO 0x40 // Serial data out is disabled (how did you get the output ??)

/* use with SetOutput() */
#define HOLD	1	#define RELEASE	2
# Appendix B. Remarks
Remark 1: BIN/2sCOMP (datasheet page 21, 22, 23)
If you are NOT planning to use this feature, connect pin 5 to VCC. This is only used in the case of bipolar output mode, where the DAC output range is from negative voltage (-5V, -10V or -10.8V) to a positive voltage ( +5V, +10V, +10.8V). For unipolar output ranges, coding is always straight binary. For this the negative supply is to be connected to pin 1 (Vss) and the positive supply to pin 24 (Vdd).

In binary mode (HIGH): The maximum DAC value sets for the most positive output. A DAC value of zero will provide the most negative output selected.A zero output voltage (switching between postive and negative output value) is achieved mid scale.

In 2scomp (LOW): The maximum DAC value with the MSB (Most Significant Bit) set to zero, will provide the maximum positive output value. A DAC value of all zero, except the MSB is set, will provide the maximum negative output. A DAC value of all zeros, will generate 0V output (switching between postive and negative output value)

Example in DAC values : AD5722 (12 bits) and pn5V
binary 2scomp
+5V	FFF 7FF
 0v	800 000
 -5V	000 800

In order to use the 2sComp instead of the default binary on bipolar:
1. connect pin 5 to comp2_pin_DAC (defined below)
2. call begin from sketch as : AD57.begin(dac, range, COMP2)

Remark 2: LDAC : load control
TIE this pin to VCC.
This pin is the hardware control to update/load the (updated) DAC values for both DAC_A and DAC_B at the same time. In this library we are using the software variant loadDac() to do the same.

When setDac(dac, value, LOAD) is called to set the value for either DAC_A, DAC_B or both DAC_AB, an optional bool LOAD can be used. When set to 0 it will not update and in the sketch you have to call loadDAC() after setting the value(s). If LOAD is not used or set to 1, it will call
loadDAC() after setting the value (default)

However IF you still want to use the hardware control, an AD57-example can be used and perform the following
1. Uncomment and set the ldac_pin_DAC (in section below)
2. Connect the LDAC pin to this pin on the Arduino
3. BEFORE updating the DAC settings call setOutput(HOLD)
4. update DAC_A and DAC_B with LOAD = 0;
5. after updating call setOutput(RELEASE) or loadDac()

Remark 3 : REFIN
The simplest way to explain is that this voltage is devided by the maximum value of the ADC bits. Say REFIN = 2,5V / 10^16 = X. If a value (Y) is written in the DAC channel, the DAC-channel amplier now receives a voltage value of X * Y = Z. That Z-value is the offset between the lowest voltage value (AVss either negative or GND) and the highest value (AVdd). It is important to have this reference voltage as stabile as possible, and you'll find that schematics use a voltage regulator. For testing however make a voltage divider. If Vcc is 5V, take 2 resistors of 1K each to make it 2.5V.